## Slide 1
CUSTOM AIO FLIGHT CONTROLLER DESIGN

## Slide 2
GOAL
Design an ultra-lightweight All-In-One Flight Controller capable of controlling an autonomous drone.
  Specifications
  Small size (25×25 mm)
  Lightweight (Target ≈3.14 g PCB)
  Long range communication
  IMU based stabilization
  ArduPilot compatibility
  Battery powered
  USB programming
  External Flash storage

## Slide 3
COMPLETE HARDWARE ARCHITECTURE

## Slide 4
POWER SUPPLY SECTION
Component: MPM3610 Buck Converter
  FUNCTION
  CONVERTS VBAT (3.0–4.2 V) TO 3.3 V
  POWERS ALL DIGITAL COMPONENTS
  HIGH EFFICIENCY (~90–95%)
  MAXIMUM OUTPUT CURRENT: 1.2 A
  SUPPORTING COMPONENTS
  C7 – 10 ΜF (INPUT FILTER)
  C8 – 100 NF (NOISE FILTER)
  C9, C10 – 22 ΜF (OUTPUT STABILIZATION)
  C11, C12 – 100 NF (HIGH-FREQUENCY BYPASS)
  Specifications
  Input Voltage
4.5V – 21V
  Output Voltage
Adjustable
  3.3V
Maximum Output Current
  1.2A
Efficiency
  Approximately 90–95%
Switching Frequency
  About 2 MHz

## Slide 6
STM32F411CEU6 – FLIGHT CONTROLLER (MAIN PROCESSING UNIT)
  ROLE IN THE SYSTEM
  CENTRAL PROCESSING UNIT (BRAIN OF THE AIO BOARD)
  EXECUTES FLIGHT CONTROL FIRMWARE
  COMMUNICATES WITH ALL ONBOARD PERIPHERALS
  GENERATES MOTOR CONTROL SIGNALS
  MANAGES WIRELESS COMMUNICATION AND SENSOR PROCESSING
  MAJOR FUNCTIONS
  READS IMU SENSOR DATA
  PROCESSES FLIGHT CONTROL ALGORITHM
  CONTROLS BRUSHED MOTORS
  STORES CONFIGURATION IN FLASH MEMORY
  COMMUNICATES WITH RF MODULE
  SUPPORTS USB PROGRAMMING AND SWD DEBUGGING

## Slide 8
  PURPOSE
  PROVIDES A STABLE CLOCK SOURCE FOR STM32
  ENSURES ACCURATE TIMING FOR ALL PERIPHERALS
  IMPROVES USB COMMUNICATION ACCURACY
  ENABLES RELIABLE SPI COMMUNICATION
CLOCK CIRCUIT (SYSTEM CLOCK GENERATION)
  COMPONENTS USED
  8 MHZ CRYSTAL OSCILLATOR (X2)
  2 × 18 PF LOAD CAPACITORS (C5, C6)
SPECIFICATIONS
  CONNECTIONS
  PH0 (OSC_IN) → CRYSTAL
  PH1 (OSC_OUT) → CRYSTAL
  C5 → CRYSTAL TO GND
  C6 → CRYSTAL TO GND

## Slide 9
RESET & BOOT CIRCUIT
  RESET CIRCUIT
COMPONENTS USED
  RESET PUSH BUTTON (SW2)
  10 KΩ PULL-UP RESISTOR (R1)
  PURPOSE
  MANUALLY RESETS THE STM32
  RESTARTS FIRMWARE EXECUTION
  USED DURING DEBUGGING AND
  FIRMWARE DEVELOPMENT
  CONNECTIONS
  NRST PIN → RESET BUTTON
  R1 (10 KΩ) → NRST TO 3.3 V
  RESET BUTTON → GND
  BOOT CIRCUIT
COMPONENTS USED
  10 KΩ PULL-DOWN RESISTOR (BOOT0)
  PURPOSE
  SELECTS THE BOOT MODE
  ENSURES BOOT FROM INTERNAL FLASH MEMORY

## Slide 10
SWD PROGRAMMING INTERFACE
  PURPOSE
  PROGRAM STM32
  DEBUG FIRMWARE
  FLASH BOOTLOADER
  REAL-TIME DEBUGGING
SIGNALS
  PROGRAMMER
  ST-LINK V2
  STM32CUBEPROGRAMMER
  ADVANTAGES
  FAST PROGRAMMING
  REAL-TIME DEBUGGING
  BREAKPOINTS
  REGISTER MONITORING

## Slide 11
USB TYPE-C INTERFACE
  PURPOSE
  FIRMWARE UPLOAD
  SERIAL COMMUNICATION
  BOARD POWER DURING PROGRAMMING
  MAIN COMPONENTS
  USB TYPE-C CONNECTOR
  CC1 & CC2 RESISTORS (5.1 KΩ)
  USB_DP
  USB_DM
SPECIFICATIONS
FUNCTIONS
  FIRMWARE UPLOAD
  USB COMMUNICATION
  FUTURE CONFIGURATION
  DEBUG LOGGING

## Slide 13
ICM42688-P INERTIAL MEASUREMENT UNIT
  PURPOSE
  MEASURES MOTION
  MEASURES ROTATION
  DRONE STABILIZATION
  FLIGHT NAVIGATION
  SENSOR TYPE
  3-AXIS ACCELEROMETER
  3-AXIS GYROSCOPE
SPECIFICATIONS
CONNECTIONS
  SUPPORTING COMPONENTS
  100 NF CAPACITOR
  2.2 ΜF CAPACITOR
FEATURES FROM DATASHEET

## Slide 15
SX1280 RF TRANSCEIVER (EXPRESSLRS 2.4 GHZ)
PURPOSE
  WIRELESS COMMUNICATION BETWEEN DRONE AND TRANSMITTER
  RECEIVES CONTROL COMMANDS
  SENDS TELEMETRY DATA
  SUPPORTS EXPRESSLRS PROTOCOL
COMPONENT
  SX1280IMLTRT
KEY SPECIFICATIONS
STM32 CONNECTIONS
FUNCTIONS
  RECEIVES RC COMMANDS
  SENDS TELEMETRY
  SPI COMMUNICATION
  LONG RANGE COMMUNICATION

## Slide 17
RF MATCHING NETWORK & ANTENNA
PURPOSE
  MATCHES ANTENNA IMPEDANCE
  MAXIMIZES RF POWER TRANSFER
  REDUCES REFLECTED POWER
  IMPROVES COMMUNICATION RANGE
COMPONENTS
  INDUCTOR
  MATCHING CAPACITORS
  2.4 GHZ ANTENNA
IMPEDANCE
  RF OUTPUT = 50 Ω
  ANTENNA = 50 Ω
BENEFITS
  MAXIMUM TRANSMISSION EFFICIENCY
  BETTER RECEIVER SENSITIVITY
  LOWER SIGNAL LOSS
  STABLE RF PERFORMANCE

## Slide 18
W25Q32JV EXTERNAL FLASH MEMORY
PURPOSE
  STORES CONFIGURATION DATA
  STORES CALIBRATION VALUES
  STORES LOGS
  SUPPORTS FUTURE
  FIRMWARE EXPANSION
  COMPONENT
W25Q32JV
KEY SPECIFICATIONS
STM32 CONNECTIONS
FUNCTIONS
  PARAMETER STORAGE
  CALIBRATION STORAGE
  FLIGHT LOGS
  FIRMWARE SUPPORT

## Slide 20
STM32G071GBU6 – MOTOR CONTROLLER
  DEDICATED MCU FOR MOTOR 2 ESC
  GENERATES SIX PWM GATE SIGNALS
  ARM CORTEX-M0+ (64 MHZ)
  SWD PROGRAMMING INTERFACE
  RESET CIRCUIT WITH PULL-UP RESISTOR
  LOCAL POWER DECOUPLING CAPACITOR
SPECIFICATIONS
  SUPPLY VOLTAGE
  OPERATING VOLTAGE
  2.0–3.6 V
  USED VOLTAGE
  3.3 V
CURRENT CONSUMPTION
  ACTUAL CURRENT DEPENDS ON
  PWM FREQUENCY
  CPU LOAD
  PERIPHERAL USAGE

## Slide 23
GATE DRIVER & POWER STAGE
  FD6288Q THREE-PHASE GATE DRIVER
  SIX AON7524 MOSFETS (3 HALF BRIDGES)
  BOOTSTRAP CIRCUIT FOR HIGH-SIDE DRIVING
  GATE RESISTORS FOR MOSFET PROTECTION
  THREE-PHASE MOTOR OUTPUT
  POWERED DIRECTLY FROM VBAT
SUPPLY VOLTAGE

## Slide 26
CURRENT CONSUMPTION & POWER BUDGET
POWER SOURCE
  BATTERY: 2S LIPO (7.4–8.4 V)
  REGULATED 3.3 V SUPPLY USING MPM3610
ESTIMATED CURRENT CONSUMPTION
DIGITAL SECTION TOTAL
  RX MODE: ≈100 MA
  TX MODE: ≈200 MA (PEAK)
MPM3610 CAPABILITY
  OUTPUT VOLTAGE: 3.3 V
  MAXIMUM OUTPUT CURRENT: 1.2 A
  SAFETY MARGIN: >80% AVAILABLE

## Slide 27
COMPLETE SYSTEM SIGNAL FLOW
  POWER FLOW
  VBAT → BUCK CONVERTER → 3.3V LOGIC SUPPLY
  VBAT → ESC GATE DRIVERS → MOSFETS → MOTORS
  DATA FLOW
  IMU → STM32F411 → FLIGHT CONTROL ALGORITHM
  EXPRESSLRS → STM32F411 → CONTROL COMMANDS
  FLASH MEMORY ↔ STM32F411
  STM32F411 → STM32G071 ×2 → ESC PWM SIGNALS
  STM32G071 → GATE DRIVERS → MOSFETS → BLDC MOTORS

## Slide 28
CONCLUSION & FUTURE WORK
PROJECT ACHIEVEMENTS
  CUSTOM 20 × 20 MM AIO FLIGHT CONTROLLER DESIGNED
  COMPLETE SCHEMATIC DEVELOPED
  COMPONENT SELECTION COMPLETED
  HARDWARE ARCHITECTURE VERIFIED
  DESIGN RULE CHECK (DRC)
NEXT PHASE
  ADD BATTERY VOLTAGE MONITORING
  ADD CURRENT SENSING CIRCUIT
  ADD ESC TELEMETRY FEEDBACK
  ADD SERVO OUTPUT HEADERS
  SUPPORT ROTORFLIGHT ADVANCED FEATURES
  INTEGRATE ESP32-S3 VISION MODULE
  ADD SONY IMX219 SURVEILLANCE CAMERA
  ADD LIVE VIDEO TRANSMISSION

## Slide 29
THANK YOU